## Slide 1
Workshop Traffic Management and Control
Weigh In Motion data
Oslo
2017-06-08
Torbjørn Haugen
Associate Professor
Traffic Engineering Research Centre
Department of Civil and Transport Engineering
NTNU

## Slide 2: Content
Introduction
Field tests 2011-2016. Results and experiences
Ongoing project WIM ATK
Future work

## Slide 3: The Demand for WIM Data
Real time data
Control of heavy vehicles (Traffic safety, competitiveness)
Historical data
Road planning, design and construction
Road maintenance
Bridge applications
Cost-benefit analysis / Environmental factors

## Slide 4: Some Terms and Definitions
Static weight: The vehicle has to stop at a weight station
(Low speed WIM: The vehicle is weighed while driving at 5-15 km/h)
High speed WIM: The vehicle is weighed while driving at the desired speed
V2I communication: New technology has made it possible to retrieve weight from sensors on the vehicle

## Slide 5: Field tests 2011-2016
Several field tests of piezo based WIM and Lineas Quarts based WIM where WIM data was compared with static weight
V2I test where weight data was retrieved directly from sensors in the vehicle

## Slide 6: Field tests 2011-2016

## Slide 7: Some Conclutions Based on Tests 2011-2016
Piezo cables have a short lifetime, and requires frequent recalibration
Lineas Quarts sensors are more expensive, but have a better accuracy and longer expected lifetime
The same sensor type can give very different results with different dataloggers
The asphalt and the road are important factors
Acceleration or breaking will affect the registered weight
Also the vehicle position affects the registered weight

## Slide 8: ATK Systems
Used for speed enforcement in Norway
More than 250 units across the whole country
Operated with piezo electrical cables
Weight data is collected but not further utilized
First tests with ATK data in 2016. Promising results.
ATK signs

## Slide 9: ATK Units
Consist out of a camera unit and two piezo electrical cables
Piezo electrical cables PATK E18 Dørdal
Camera unit PATK E18 Dørdal

## Slide 10: First Results 2016

## Slide 11: Quality Indicators
Relative stable weight of the1st axle of 6 axle vehicles
Used as a quality indicator for a ATK unit
Axle weight distributions for 6 axle vehicles on SATK E6 Åsen / Nord-Trøndelag

## Slide 12: Field Test 2017
Axle weight distribution of 6ax semi trailer at PATK Auråen E18 Telemark

## Slide 13: Field Test 2017
Chart: Dynamic vs. static GW ATK Auråen / E 18 Telemark
y=x | 0 | 70
Comparison of static gross weights and ATK data

## Slide 14: Field Test 2017
Comparison of static gross weights and ATK data. Calibration factor (1,15)
Chart: Dynamic vs. static GW ATK Auråen / E 18 Telemark
y=x | 0 | 70

## Slide 15: Next Steps
Identification of different vehicle classes and their axle and gross weights to adjust calibration method
Develop different calibration method for different vehicle classes
Further statistical analytics and field tests in different parts of the country
Gaining information about weight statistics from as many ATK points as possible
V2I – communication for calibration

## Slide 16
Thank you for Your attention!
Questions ?
Torbjørn Haugen, torbjorn.haugen@ntnu.no
Ass. Professor, Traffic Engineering Research Centre, NTNU