## Slide 1
Managed motorways
Seminar Traffic Management and Control
June 8th 2017, Thon Hotel Bristol, Oslo
Arvid Aakre
Traffic Engineering Research Centre
Department of Civil and Environmental Engineering, NTNU
E-mail: arvid.aakre@ntnu.no

## Slide 2: Content
Introduction
Terminology; Managed motorway, Capacity and Productivity
Brief summary of the Motorway Capacity Guide
Measurement results
Recommended values for design
Future work
Some comments on Norwegian and Nordic conditions

## Slide 3: Introduction - background
Motorway Capacity Guide Part 1: Metropolitan Managed Motorways (Draft May 2017)
Authors: John Gaffney and Hendrik Zurlinden, VicRoads, Melbourne, Australia

## Slide 4: Introduction – Melbourne motorway network
Melbourne is the capital of Victoria southeast in Australia
Area ~ 10.000 km2 (~ Oslo + Akershus + Østfold)
Population ~ 4.6 mill (~ Slightly less than Norway)
Motorway network covers
  7% of the urban arterial road lane kms
  40% of the urban arterial road travel (increasing)
  M1 corridor from west to east of the map is about 70 km

## Slide 5: Introduction - M1 Corridor
70 km motorway corridor
Total entering volume ~ 900.000 vehicles a day
More than 1 million trips each day (1.2 persons per vehicle)

## Slide 6: Speed limits and enforcement
Australian urban motorways have a maximum speed limit of 100 km/h
A very active and strict enforcement regime
In Victoria the tolerance is only +3 km/t
-> relative small speed differences

## Slide 7: Managed motorways
A managed motorway is a motorway which uses different traffic management measures to enhance quality of traffic flow
Examples of such measures are variable speed limits, ramp metering, hard shoulder running, traffic information, alternative routes, ITS measures, lane signals, traffic data collection and monitoring, incident detection etc
John Gaffney: «A congested motorway is a poorly managed motorway»
https://www.youtube.com/watch?v=XCEBpgEv_QQ
https://www.youtube.com/watch?v=SYbceSqk_Mk

## Slide 8: Capacity
«The maximum sustainable flow rate at which vehicles or perons can be expected to traverse a point or uniform segment of a lane or roadway during a specified time period under given roadway, geometric, traffic, environmental and control conditions» (HCM 2016)
Capacity values are measured at active bottlenecks and determined on the basis of systematical analysis of data to capture the effect of systematic and random fluctuations under a wide range of demand patterns

## Slide 9: Capacity
Capacity should be based on long-term measurements
Should not use short term traffic counts on a single day
Each dot above is a one hour measurement

## Slide 10: Factors impacting on capacity
Cross section
  Lane and shoulder width
  Visibility
Alignment
  Gradient
  Curvature
  Sags and crests
Traffic
  Vehicle type distribution
Location
  Share of commuters
Other
  Merge, diverge, weaving
  Auxiliary lanes
  Acceleration, deceleration lanes
Traffic management
Ramp metering
Maintenance
Work zones
Enforcement regime
Driver behaviour
  Headways
  Braking
  Lane changing activity
  Compliance with road rules

## Slide 11: Productivity
Productivity is defined as the product of traffic speed and traffic flow
Unit is vehicle-kilometers travelled on a road segment per time unit
High productivity is achieved when both traffic flow and traffic speed are maintained near maximum values
Efficient energy use align closely with the point where the motorway operates at maximum productivity
Productivity is a good measure for efficiency, safety as well as environmental conditions

## Slide 12: Measurements
Please remember, a flow rate of 1800 veh/hour means:
  an average time headway (front-front) of 2 seconds
  An average time gap (front-back) of about 1.8 sec (depending on speed and vehicle length)

## Slide 13: Measurements
No interaction between sections; elimination of downstream bottlenecks (above)
Interaction between sections, no elimination of downstream bottlenecks (below)

## Slide 14: Recommended values for design
Design values are typical about 90% of observed capacity
See also more complex theoretical methods and models

## Slide 15: Managed motorway – probability for breakdown

## Slide 16: Managed motorway – probability for breakdown

## Slide 17: Design of unmanaged and managed motorways
Design of unmanaged motorways (above)
Design of managed motorways (below)

## Slide 18: Future work and investigations
Merging, diverging and weaving
Differences between unmanaged and managed motorways
Capacity loss and recovery
Congestion and safety
Lane changing activity and capacity
Effect of geometric parameters and heavy vehicles

## Slide 19: What about Norwegian / Nordic conditions?
Swedish guidelines are reviewed in the Australian Motorway Capacity Guide together with the US (HCM), UK, German and Dutch guidelines
We have limited experiences with Norwegian conditions, but the values from Australia seems to be useful also in Norway
Norwegian motorways have a very limited degree of management
There is a large potential for improvement

## Slide 20: Thank you for your attention
Arvid Aakre NTNU Traffic Engineering Research Centre Norwegian University of Science and Technology Trondheim, NORWAY
E-mail: arvid.aakre@ntnu.no