## Slide 1
Traffic flow and driver behaviour
Seminar Traffic Management and Control
June 8th 2017, Thon Hotel Bristol, Oslo
Arvid Aakre
Traffic Engineering Research Centre
Department of Civil and Environmental Engineering, NTNU
E-mail: arvid.aakre@ntnu.no

## Slide 2: Outline of the presentation
Introduction
Driver behavior and efficiency
Saturation flow rate at traffic signals
Driver behavior – competition or cooperation ?
Cooperation at roundabouts
Merging, diverging and weaving
Discussion

## Slide 3: Driver behaviour and efficiency
Driver behaviour is an important factor to increase capacity when needed
Driver assistance systems might increase attention, safety and efficiency

## Slide 4: Saturation headway and saturation flow rate – model 1
 | Parameter | Typical value
hs | Saturation headway | 1.8 - 2.0 sec
tr | Queue dep. reaction time | 1.0 - 1.5 sec
sj | Jam spacing | 7 - 10 m
vs | Saturation speed | 40 - 60 km/h
vc | Queue clearance wave speed | 20 - 30 km/h
S | Saturation flow rate | 1800 - 2000 veh/h

## Slide 5: Saturation headway and saturation flow rate – model 2
 | Parameter | Typical value
hs | Saturation headway | 1.8 - 2.0 sec
ss | Saturation spacing | 20 - 30 m
vs | Saturation speed | 40 - 60 km/h
S | Saturation flow rate | 1800 - 2000 veh/h

## Slide 6: Example from Trondheim

## Slide 7: Experiments – field trials at a closed track
2016 Hell Motor Arena
22 cars
20 runs
2 different scenarios
1999 Tiller
10 cars
26 runs
6 scenarios

## Slide 8: Results 1999 – Finding the limit for efficency

## Slide 9: Results 2016 – Saturation flow rate

## Slide 10: Observed headway distributions

## Slide 11: Satisficing or optimizing?
Driver assistance system

## Slide 12: How does driver behavior affect delay?
Example from Trondheim
Aimsun micro simulation
100 replications

## Slide 13: How does driver behavior affect delay?

## Slide 14: Traffic flow at bottlenecks
In the active bottleneck:
Driver attention
Increase capacity
Minimize lost time
20-30 % capacity increase is feasible, just from driver behavior
Use driver assistance system?
Upstream intersections with Downstream Flow Restrictions:
Distribute priority
Minimize delays for those not heading for the bottleneck
Minimize stress and aggression
Green time is not optimal for distributing priority in DFR conditions!

## Slide 15: Conclusions – driver behavior and efficiency
Driver support systems can provide assistance based on position and traffic conditions
Experiments have shown that there is a great potential for enhanced driver behavior
Doubling throughput is possible (with maximum effort)
Efficiency gains of 20 % may be obtained without drivers leaving the comfort zone, and without sacrificing safety margins
Simulations have shown that such efficiency gains lead to significant delay reductions
The challenge is that your willingness to be efficient leads to reduced delays for those following you. There’s no immediate reward …

## Slide 16: Road traffic - Competition or cooperation?
Competition has been shown to be useful
up to a certain point and no further,
but cooperation, which is the thing we must strive for today,
begins where competition leaves off.
Franklin D. Roosevelt
If you want to make peace with your enemy,
you have to work with your enemy.
Then he becomes your partner.
Nelson Mandela

## Slide 17: Cooperation in roundabouts

## Slide 18: Affecting gaps offered to yielding drivers
Adapted from figure 8.14
Revised Monograph on traffic flow theory
Chapter 8: Troutbeck and Brilon (2001)

## Slide 19: Results - Roundabout
Delay per lap | Experiment 1 A | Experiment 2 A | B < A?
Average [sec] | 72 | 49 | Yes
Confidence interval | 67-77 | 45-53 | 

## Slide 20: Zipper merging
All merging of traffic movements in Norway is done as zipper merging
  Lone drop from 2 to 1 lane
  Entry to a main road with acceleration lane
  Other merging situations
The lanes have equal rights; 50/50 priority
The merging should be made within a certain area

## Slide 21: Cooperative zipper merging

## Slide 22: Uninstructed vs Instructed Zipper Merge

## Slide 23: Results zipper merging

## Slide 24: Conclusions
Cooperation in traffic seems to
Lead to more favorable gap distributions
Slightly reduce critical gap and follow-up headway
Increase capacity
Reduce delays
Observed effects:
Capacity increases of 20-30 % were obtained without sacrificing safety
Drivers tend to understand the instructions given to them, and they are also capable of turning advice into behavior change
By cooperating, instead of competing, “everybody” wins
The challenge is that your willingness to cooperate leads to reduced delays for those following you. There’s no immediate reward…

## Slide 25: Thank you for your attention
Arvid Aakre NTNU Traffic Engineering Research Centre Norwegian University of Science and Technology Trondheim, NORWAY
E-mail: arvid.aakre@ntnu.no